Lunar Reconnaissance Orbiter Project

LYMAN ALPHA MAPPING PROJECT

EXPERIMENT DATA RECORD (EDR)

DATA PRODUCT

SOFTWARE INTERFACE SPECIFICATION

June 2009

SwRI® Project 11239

Document No. 11239-EDRDP_SIS-01

Rev 1 Chg 0

Contract NNG05EC87C

Prepared by

David E. Kaufmann

Lunar Reconnaissance Orbiter Project

LYMAN ALPHA MAPPING PROJECT

EXPERIMENT DATA RECORD (EDR)

DATA PRODUCT

SOFTWARE INTERFACE SPECIFICATION

SwRI® Project 11239

Document No. 11239-EDRDP_SIS-01

Rev 1 Chg 0

Contract NNG05EC87C

Prepared by:  David E. Kaufmann					04 June 2009

Approved by:  ____________________________________	Date:  ____________

Maarten Versteeg, (SwRI) LAMP Software Lead

Approved by:  ____________________________________	Date:  ____________

Rafael Alanis, (JPL) PDS Imaging Node

Approved by:  ____________________________________	Date:  ____________

Sue Lavoie, (JPL) PDS Imaging Node Co-Manager

Approved by:  ____________________________________	Date:  ____________

Stan Scott, (GSFC) LRO Science Data Manager

Approved by:  ____________________________________	Date:  ____________

Edwin Grayzeck, (GSFC) PDS Program Manager

Approved by:  ____________________________________	Date:  ____________

Joel Parker, (SwRI) LAMP SOC & Archive Manager

Approved by:  ____________________________________	Date:  ____________

Randy Gladstone, (SwRI) Acting LAMP PI

Approved by:  ____________________________________	Date:  ____________

Joerg Gerhardus, (SwRI) Quality Assurance

Approved by:  ____________________________________	Date:  ____________

Sarah Hodgson, (SwRI) Project CM

TABLE OF CONTENTS

Page

1.	Purpose and Scope of Document	1

2.	Applicable Documents	1

3.	Relationships with Other Interfaces	1

4.	Data Product Characteristics and Environment	2

4.1	Instrument Overview	2

4.2	Data Product Overview	3

4.3	Data Processing	4

4.3.1	Data Processing Level	4

4.3.2	Data Product Generation	5

4.3.3	Data Flow	5

4.3.4	Labeling and Identification	5

4.4	Standards Used in Generating Data Products	6

4.4.1	PDS Standards	6

4.4.2	Time Standards	6

4.4.3	Coordinate Systems	6

4.4.4	Data Storage Conventions	6

4.5	Data Validation	6

5.	Detailed Data Product Specifications	6

5.1	Data Product Structure and Organization	7

5.2	Data Format Descriptions	7

5.3	Label and Header Descriptions	8

6.	Applicable Software	8

6.1	Utility Programs	9

6.2	Applicable PDS Software Tools	9

6.3	Software Distribution and Update Procedures	9

Appendix A – Detailed LAMP EDR FITS File Specifications	10

Appendix B – Glossary	20

Appendix C – Acronyms and Abbreviations	21

Appendix D – NASA and CODMAC Data Level Definitions	22

Appendix E – Example PDS Label	23

REVISION NOTICE

| Change | Date | Affected Portions |
| --- | --- | --- |
| Initial draft | 16 April 2007 |  |
| Draft 1 | 01 June 2007 | Updated draft, incorporating comments from Stan Scott and Karen North Section 4.2, Data Product Overview (added reference to Section 5 and Appendix A) Section 4.3, Changed reference to section 3 to Section 5 instead |
| Draft 2 | 05 August 2007 | Updated draft, incorporating comments from Rafael Alanis Signature page added Appendix A - Detailed LAMP EDR FITS File Specifications, removed TBD items in FITS Extensions 2, 3, 5, and 6 Appendix E - Example PDS Label, provided an updated (and corrected) label |
| Draft 3 | 15 February 2008 | Updated draft, incorporating comments from the SIS reviewers Miscellaneous small corrections and additions |
| Draft 4 | 24 February 2008 | Updated Ed Grayzeck’s location per Stan Scott’s email; added LRO epoch specification to description of SCUT Signature page; Section 4.4.2 |
| Draft 5 | 15 December 2008 | Removed final TBD/TBS items Title page; Section 2 |
| Draft 6 | 02 February 2009 | Added clarifying text; reformatted |
| Draft 7 | 06 February 2009 | Added primary FITS header keyword, HVOPSLVL Appendix A |
| Draft 8 | 09 February 2009 | Removed “consecutive” from description of Calculated Count Rate extension; clarified SCUT time stamp in EDR filename to refer to the start of the file rather than the start of the first data acquisition in the file Section 4.2; Section 4.3.4 |
| Initial Issue R0 | 03 March 2009 | Added text to Calculated Count Rate extension description to say that if no pixel list data are present, the data portion of the extension would be empty. Section 4.2 |
| Revision 1 | 04 June 2009 | Appendix E – Example PDS Label, placed quotes around the values of SPACECRAFT_CLOCK_START_COUNT and SPACECRAFT_CLOCK_STOP_COUNT |

# Purpose and Scope of Document

The purpose of this Data Product SIS is to provide users of the LAMP EDR (CODMAC Level 2) data product with a detailed description of the product and a description of how it was generated, including data sources and destinations.  The EDR product contains time-tagged sequences of uncalibrated far-UV photon detections (when LAMP is operated in pixel list mode) and/or uncalibrated far-UV spectral images (when LAMP is operated in histogram mode).  Housekeeping data, which will be used to interpret the raw data, are also included.  This SIS is intended to provide enough information to enable users to read and understand the data product.  The users for whom this SIS is intended are the scientists who will analyze the data, including those associated with the Lunar Reconnaissance Orbiter Project, and those in the general planetary science community.

This Data Product SIS describes how the data in the EDR data product are acquired by the LAMP instrument, and how they are processed, formatted, labeled, and uniquely identified.  The document discusses standards used in generating the product and software that may be used to access the product.  The data product structure and organization is described in sufficient detail to enable a user to read the product.  Finally, an example of a product label is provided.

# Applicable Documents

This Data Product SIS is intended to be consistent with the following documents:

- Planetary Data System Standards Reference, version 3.7, March 20, 2006, JPL Document D-7669, Part 2.

- Planetary Science Data Dictionary Document, revision E, August 28, 2002, JPL Document D-7116.

- Lunar Reconnaissance Orbiter Data Management and Archive Plan, 431-PLAN-000182.

- LRO LAMP Instrument Team Data Management and Archive Plan, 11239-DMAP-01.

- Interface Control Document for the LRO Ground System, 431-ICD-000049.

- LAMP Science Team and PDS Imaging Node Interface Control Document, JPL Document D-49057.

- Lyman Alpha Mapping Project Experiment Data Record (EDR) Archive Volume Software Interface Specification, 11239-EDRAV_SIS-01.

- Definition of the Flexible Image Transport System (FITS), version 2.1b, December 9, 2005, IAU FITS Working Group (http://fits.gsfc.nasa.gov/iaufwg/).

- “LAMP: the Lyman Alpha Mapping Project aboard the NASA Lunar Reconnaissance Orbiter mission,” by Gladstone, G. Randall, Stern, S. Alan, Retherford, Kurt D., Black, Ron, Scherrer, John R., Slater, David C., Stone, John M., Feldman, Paul D., and Crider, Dana, in Astrobiology and Planetary Missions, edited by Hoover, Richard B., Levin, Gilbert V., Rozanov, Alexei Y., and Gladstone, G. Randall, Proceedings of the SPIE, Sep. 2005, Vol. 5906, pp. 380-388.

# Relationships with Other Interfaces

The LAMP EDR Archive Volume SIS [7] describes how the data products specified by this document will be made available through the PDS, and could be affected by a change in this SIS.

# Data Product Characteristics and Environment

This section describes the LAMP EDR data product in greater detail, including how the data are acquired, the types of data in the EDR, and how the data are processed and validated.

## Instrument Overview

The LAMP UV spectrograph instrument is largely based on the Pluto ALICE instrument flying on board the New Horizons spacecraft.  (The Pluto ALICE design, in turn, is based largely on the design of the Rosetta ALICE instrument.)  LAMP consists of a telescope, a Rowland-circle spectrograph, and an electronics section; it also includes an extended forward light baffle, a pair of Lunar Terminator Sensors (LTS), and a thermal radiator.  The telescope mirror collects incoming light that passes through the entrance aperture at the front end of the instrument and directs it towards the entrance slit of the Rowland-circle imaging spectrograph.  The spectrograph contains a reflective holographic diffraction grating and a UV-sensitive, solar-blind, 2-D open-structure microchannel plate detector located on the Rowland circle.  The detector electronics, command and data handling (C&DH) electronics, and power supply section is located directly behind the spectrograph section next to the detector.  LAMP has a passband of 57.5-196.5 nm and a pixel format of 1024 spectral by 32 spatial pixels.

The detector system outputs to the C&DH electronics the pixel location for each detected photon event, a location consisting of a spectral and a spatial coordinate.  The first (x) dimension provides the spectral location of the detected photon and the second (y) dimension provides one-dimensional spatial information.  The events are processed by its own C&DH electronics.  The C&DH is also the controller of the LAMP instrument; it receives commands from the spacecraft, acquires data from the MCP detector system, and returns telemetry to the spacecraft.  Science data generation is performed by the detector hardware, but the C&DH also controls this function.

The LAMP instrument has two acquisition modes in which the spectral/spatial data from the detector are processed by the C&DH subsystem.  The main LAMP data acquisition mode is the pixel list acquisition mode.  In this mode the instrument stores photon event data as they arrive from the detector system.  In order to provide timing information, “time hacks” are inserted into the data stream at a programmable interval between 4 and 512 msec.  In addition, LAMP provides a histogram acquisition mode.  This mode is mainly used for calibration acquisition operations and allows for long integrations to obtain observations of faint sources with high signal-to-noise ratios.  In histogram acquisition mode, the detector accumulates the number of events that are occurring at each of the 1024 x 32 pixel “locations” provided by the detector electronics over a period of time.

The LTS has been added to protect the highly-sensitive LAMP instrument from observing the relatively bright daylit regions of the Moon with the aperture door open, either by lowering the detector high voltage or closing the aperture door.  The design of the LTS uses redundant Si PN photodiode detectors and amplifier electronics which are fed by an externally mounted mechanical collimator that oversamples the LAMP field of view.  The LTS field of view is 1º x 10º for both a “forward” photodiode (parallel to the LAMP slit but canted at 1.5º ahead of the track of the LAMP boresight) and an “aft” photodiode (parallel to the LAMP slit but canted 1.5º behind the track of the LAMP boresight).  When both sensors are operating simultaneously, the signal from these two diodes are each differenced at a 10-Hz rate with “dark” photodiodes (to correct for temperature effects) and combined (in a programmable way) to provide LAMP’s response to the crossing of the terminator (from day to night or vice versa).  LAMP can also operate with only a single working LTS.  In fact, this will be the standard mode of operation when only a single LVPS is being used.  Depending on the orientation of the LRO spacecraft, the forward and aft LTS photodiodes will switch roles several times during the mission.  The LAMP aperture door has a small (1.0 mm diameter) hole in it which allows dayside observations at about the same count rate with the door closed as are observed on the night side when the aperture door is open.  The LRO mission plan calls for using the LTS to lower and raise the detector high voltage until minimum LAMP experiment objectives are met, then using the LTS to close and open the aperture door to allow continuous LAMP day and night side observations for the remainder of the mission.

## Data Product Overview

The sources of the data contained in the LAMP EDR data product are files received from the LRO MOC containing (1) the LAMP instrument low-speed housekeeping telemetry and (2) the LAMP science data.  These files are delivered on a nominal basis of one file of each type per orbit.  The LAMP EDR data product combines these file pairs, also on a one file per orbit basis, into a single FITS formatted file containing the following seven types of data:

- Spectral Image (Aperture Door Open):  This is a reconstructed histogram generated from the pixel list data in the science data file.  Using information from the housekeeping data, only the pixel list data acquired when the aperture door was open are included in this dataset.  If housekeeping data are unavailable, all pixel list data are included in this histogram.  If the science data file contains only data acquired with LAMP operating in histogram mode, this dataset will contain a copy of the first histogram image. This summary image is used as a “quick-look” check on data quality. [Extension 0 = primary FITS header and data unit (HDU)]

- Spectral Image (Aperture Door Closed):  This is similar to the first dataset, but the reconstructed histogram here is generated from pixel list data acquired when the aperture door was closed.  If housekeeping data are unavailable, this dataset will be empty.  If the science data file contains only data acquired in histogram mode, this dataset will contain a copy of the second histogram image in the file. This summary image is used as a “quick-look” check on data quality. [Extension 1]

- Acquisition List:  This dataset contains a list of the generated frame acquisitions as determined from the housekeeping data file. The list includes, for each frame, the instrument frame sequence number, start and stop times, mode type, aperture door and other instrument state information. The frame acquisition times and instrument state data contained in this list are used to cross-reference with the pixel list mode data for purposes of selecting data and checking timing consistency. [Extension 2]

- Raw Frame Data:  This dataset contains all of the raw data from the science data file except for the file header. [Extension 3]

- Calculated Count Rate:  This dataset contains a high-resolution sequence of UV photon count rates computed from the pixel list data for each acquisition (nominally the whole orbit).  The resolution of this count rate sequence depends on the commanded “hack time” interval.  If no pixel list science data are available, e.g., if data are acquired only in histogram mode, then this dataset will be empty.  (The lower-resolution [1 Hz] count rate data are available in all cases in the housekeeping [Extension 6] dataset.)  This sequence will be used to assess the variation in bulk far-UV signal throughout the orbit, and may be especially useful when trending data obtained near the terminator or during exceptional events (e.g., solar flares). [Extension 4]

- LTS Data:  LAMP housekeeping data contain up to 10 values per second of gain and offset corrected measurement values from each of the two LAMP Lunar Terminator Sensors (LTS).  This dataset provides the full 10-Hz LTS dataset. These coincident LTS data will be used with the count rate sequence in Extension 4 to confirm that LAMP is viewing the appropriate day/night/shadow scenes. (Raw 14-bit LTS data sampled at the 1 Hz HK rate is included together with this 10-Hz gain and offset corrected LTS dataset in the housekeeping data Extension 6.) [Extension 5]

- Housekeeping Data:  This dataset contains the complete housekeeping dataset, both in raw format and, where applicable, in calibrated engineering units. HK data are included here to assist with joint instrument and data quality trending analyses (foreseen and unforeseen). [Extension 6]

The primary data in the LAMP EDR product files will be contained in the raw data frames in Extension 3 of the FITS files.  Nominally, LAMP will operate in pixel list mode.  In this mode the data frames will contain a series of time-tagged UV photon detection events.  The histogram images in the primary FITS header and data unit (HDU) and Extension 1 will simply be these photon events histogrammed into the 1024 spectral by 32 spatial bins.  The primary HDU (Extension 0) histogram will be generated from photon events detected on the night side of the Moon (with the aperture door open), the Extension 1 histogram from dayside data (through the pinhole opening with the aperture door closed).  Thus, these histograms will contain UV spectral images spatially smeared over the night (Extension 0) and day (Extension 1) sides.  These histograms are included up front because most FITS viewers expect image data in the primary HDU and because they can give at a glance an indication of the data quality and an average spectrum over the day and night swath(s).  LAMP can operate in histogram mode as well (e.g., for taking calibration or limb data).  In these cases the data contained in the raw frames will already be histogrammed, and the primary (Extension 0) and Extension 1 HDUs will simply contain copies of the first and second histograms.  The Acquisition List is simply a list of each LAMP data frame’s start and stop times, the mode (pixel list or histogram), aperture door state (open or closed), and LTS state (day or night).

The primary (Extension 0) FITS header contains standard file information, data acquisition start and stop times, target name, average instrument temperatures and voltages, and many other useful data pertaining to each EDR data product file.  Standard “TARGET” parameter values include “MOON,” “HDxxxxxx” (i.e., calibration stars identified by their Henry Draper Catalog numbers), “ATMOSPHERE,” “EARTH,” and “SKY.”  Other special targets such as planets and comets may be included and named at a later time.  Diagnostic items such as minimum, average, and maximum count rates and total counts, and instrument modes are also listed in the primary header.  These are file-averaged summaries of more detailed information from the instrument housekeeping data (Extension 6).

Detailed specifications for the LAMP EDR data product can be found in Section 5 and Appendix A of this document.

## Data Processing

Data format is described in Section 5, Detailed Data Product Specifications.  Data volume will vary because it is a function of the UV photon detection rate and the instrument mode.  In the nominal case, the LAMP low-speed housekeeping telemetry data file will consist of one 128-byte packet per second for the duration of the approximately 113-minute LRO orbit (~6780 packets), plus a 64-byte file header.  The LAMP science data file will consist of a number of raw instrument-generated 65536-byte frames, each preceded by a 6-byte acquisition (completion) time field, plus a 64-byte file header.  As mentioned above, the exact number of science data frames will vary from file to file.  For nominal operations in pixel list mode with a 4-msec hack rate, LAMP is expected to generate approximately 285 data frames per orbit when taking data over the entire orbit.

### Data Processing Level

The LAMP EDR data product contains raw UV photon detections/spectra and associated data corresponding to CODMAC Level 2 (see Appendix D).

### Data Product Generation

In the nominal operational sequence, the LAMP instrument will generate one low-speed telemetry file and one science data file for each orbit.  Once per day these LAMP-generated files will be retrieved from the spacecraft by the LRO MOC and then transferred by the MOC to the primary LAMP SOC pipeline computer.  The LAMP SOC pipeline “executive” program will execute once per day and detect the newly delivered data files.  After cataloging the received files, the “executive” program will initiate execution of the LAMP SOC data processing pipeline. The first element (nicknamed “Lima”) of the pipeline will be responsible for converting the data files received from the MOC into the EDR data products whose format is described in this SIS.  No calibrations will be applied to the science data at this stage.  As mentioned previously, raw telemetry values will be converted to engineering units where applicable; however, both raw and converted values will be included in the EDR data product.  Multiple versions of the output EDR products may be made available if software bugs affecting the output data are uncovered and corrected.  In the event of an error whose correction alters released data, the data will be reprocessed by the revised software and made available.

### Data Flow

The original source of the data contained in each LAMP EDR data product will be the LAMP instrument itself.  As mentioned above, LAMP-generated data files will be retrieved from the LRO spacecraft by the LRO MOC and then transferred to the LAMP SOC for further processing.  The details of this latter transfer mechanism are described in [5].  After the LAMP EDR data products are produced by the LAMP SOC, they will be archived (see [7]) and transferred to the PDS Imaging Node for permanent storage and public access.  The details of this transfer mechanism are described in [6]. The LAMP EDR data products will be delivered to the PDS Imaging Node in sequential data releases at three-month intervals as specified in Table 3 of [4].

As mentioned above, the input per-orbit housekeeping and science data files will have sizes of approximately 848 kB and 17.8 MB, respectively.  Including the additional datasets specified above for each LAMP EDR data product, and allowing for approximately 12.75 orbits per day, the total daily volume of LAMP EDR data products produced will be approximately 0.275 GB.  Over the 365 days of the nominal LRO mission, total EDR data product volume will be approximately 100 GB.

### Labeling and Identification

The dataset ID provided by the PDS for the LAMP EDR data product is:

LRO-L-LAMP-2-EDR-V1.0

The version number is incremented should the entire EDR dataset be revised.

The file naming convention for LAMP EDR data files is LAMP_ENG_nnnnnnnnnn_vv.FIT.  The ten-digit nnnnnnnnnn value will be a time stamp value, namely the Spacecraft UT (SCUT) of the start of the file.  The two-digit vv value will be a version number to facilitate unique identification of (possibly reprocessed) EDR data files.  The .FIT extension indicates that the EDR data files will be in FITS format.  Each EDR file will have a detached PDS label in a separate file of the same name, but with extension .LBL.  The label file is stored in the same directory as the FITS data file that it describes.

## Standards Used in Generating Data Products

### PDS Standards

The LAMP EDR data product complies with Planetary Data System standards for file formats and labels, as specified in the PDS Standards Reference [1].

### Time Standards

Each LAMP housekeeping and science data file that is received from the LRO MOC contains a 64-byte header specifying, among other things, the SCUT (Spacecraft Universal Time) when the file was opened for writing and when the file was closed.  SCUT is measured in seconds and fractional seconds elapsed since the epoch of the LRO mission timeline, 00:00 UTC January 1, 2001.  Within the LAMP housekeeping dataset, each packet is stamped with the instrument time when the packet was generated.  Instrument time will nominally be synchronized to SCUT as sent to LAMP by means of the time synchronization message.  Within the science dataset, the SCUT for the start and stop times of a given data acquisition are determined by correlation with the housekeeping data.  For data taken in histogram mode, there is no finer time resolution available.  For data taken in pixel list mode, “time hacks” are inserted into the UV photon event data stream at a command-modifiable interval of between 4 msec and 512 msec.  The nominal time hack interval is planned to be the minimum of 4 msec in order to provide the highest possible time resolution for the data taken in pixel list mode, the nominal operational mode for LAMP.  Finally, while it is possible to convert SCUT to UTC using the NAIF SPICE toolkit and the appropriate LRO SPICE SCLK clock correlation file, it is not currently planned to include SCUT conversions to UTC in the LAMP EDR data product.

### Coordinate Systems

The LAMP EDR data product is a CODMAC Level 2 product.  As such, the data contained therein have not been calibrated or located in space.  Thus, it is not currently planned to include spatial coordinate information in the LAMP EDR data product itself.

### Data Storage Conventions

The LAMP EDR data product complies with the FITS standard for file formats and data storage conventions, as specified in the Definition of the Flexible Image Transport System (FITS) [8].

## Data Validation

LAMP EDR data products will be validated by the LAMP Team for science content and for compliance with PDS archive standards [1].  Further details on the validation of LAMP data can be found in [3] and [4].

# Detailed Data Product Specifications

The LAMP EDR data products shall be grouped into directories with one directory per flight day.  Flight day is defined to be midnight-to-midnight UTC.  Within each directory shall be labels containing pointers to the corresponding individual data products.

## Data Product Structure and Organization

In the DATA directory of the EDR archive, data for each flight day will be in a subdirectory named in the format YYYYDDD, indicating the year and day of year for the date of the start of data acquisition.

## Data Format Descriptions

The seven types of data included in the LAMP EDR data product are listed in Section 4.2.  All of these data are stored in a single FITS file with a detached PDS label.  Each data type within the FITS file is stored in a separate HDU (Header and Data Unit).  The first two data types, the reconstructed histograms, will be stored as FITS images within their HDUs, the acquisition list will be stored as a FITS ASCII table, and the remaining data types will be stored as FITS binary tables.  A detailed listing of the proposed FITS format of the LAMP EDR data product is given in Appendix A.

A discussion of the interpretation of the frame data (FITS Extension 3) is warranted here. As described in the sample PDS header in Appendix E of this document, the binary frame data table consists of two columns.  The first column gives the generation time of the frame as an 8-byte double precision value expressing the number of integral and fractional sections elapsed since the epoch used for SCUT.  The second column contains the 32768 words (2-byte integers) of the data frame itself.  The interpretation of the data in the frames depends on the acquisition mode (pixel list vs. histogram).

In order to identify the science data frames (packets), a single 16-bit word header starts the frames.  The header is generated by the acquisition hardware and includes the information listed in Table 5-1.

Table 5-1: LAMP Science Frame Header

| Field | Size in bits | Description |
| --- | --- | --- |
| Frame contents (MSB) | 1 | 0 - pixel list 1 – histogram |
| Memory | 1 | 0 - ping (side A), 1 - pong (side B) |
| Last frame | 1 | 0 - intermediate frame 1 - last frame (acquisition cycle terminated) |
| HW acquisition | 1 | HW controlled acquisition (hardware limp along), overrides software control after 8 consecutive watchdog timeouts (see C&DH hardware documentation) |
| Frame number | 12 | Least significant 12 bits of the frame number |

In pixel list mode, each word (32767) in the remainder of the frame either describes a photon event or a time hack.  For photon events bit 15 is set to zero and time hacks are indicated by bit 15 with a value of one.  A photon event encodes the location of the detected event consisting of a 10-bit encoded spectral location and a 5-bit encoded spatial location in the remaining 15 data bits.  The time hack is used to provide temporal information about the photon events.  The acquisition hardware will generate and insert time hacks in the frame on a periodic basis (configurable for each acquisition in a range of 4 – 512 msec). In the remaining 15 bits, the time hack contains an incrementing counter that counts the number of 4 msec periods.  This value allows for data recovery in case of lost frames (packets).

In histogram mode, each word (32767) in the remainder of the frame contains the number of photon events detected for that specific spectral/spatial location.  This corresponds to considering the full frame as a two dimensional array of 32 (spatial) x 1024 (spectral) 16-bit counters stored row-wise (corresponding to the spectral dimension).  These counters saturate at a maximum value of 65535 to indicate a completely filled counting bin, meaning that the counters do not wrap around.  In addition some special data words (header and pulse height distributions) are overlying the lower left-hand corner of the actual array in a block of 4 (spatial) x 32 (spectral) words.  This usage does not limit science data contents as no detector events occur in this region. Of this over-written block, the first row contains the header word and the second and third row contain the 64 words of pulse height information.  The remainder of this block is filled with zeros.  The pulse height information is again a list of counted occurrences, but for the pulse height (event amplitude) of the separate events.  Pulse height is available in 6-bit resolution resulting in 64 bins.  These counters also saturate to a value of 65535.  So a single photon event is counted both in the spectral/spatial array and in the pulse height list.

Finally, we present a few more words of explanation about the LTS data (Extension 5). All downlinked LTS data are included in the LAMP housekeeping packet. These consist of two separate data types that are generated and collected by the instrument:

- Raw LTS data consisting of 14-bit values (0-16383 counts) at a rate of one value per LTS per housekeeping packet. The instrument collects these 14-bit raw values at a rate of 10 Hz, but only the one most recent value (i.e., the last in the previous series of ~10 samples) is reported in the HK packet for each LTS.

- Corrected LTS data, i.e., gain and offset corrected onboard, consisting of 8-bit values (0-255), generated at a rate of 10 Hz.  All such values for each LTS from the previous second (up to 10 values each) are collected and reported in the HK packet.

The 14-bit raw LTS values are gain and offset corrected into 8-bit values onboard, separately for each LTS. These values are used for the LTS light/dark function control of the aperture door. The corrected LTS data are reordered and provided in Extension 5 of the EDR FITS file for convenience as the final “LTS Data” product, which is then used to verify that the proper threshold values are selected. The raw and corrected LTS data in Extension 6 (“Housekeeping Data”) are used to verify correct operation of the LTS, but remain within the inconvenient housekeeping packets (e.g., the time hack clock and spacecraft clock must first be synchronized during extraction from the packets).

## Label and Header Descriptions

Each LAMP EDR data file is described by a PDS label in a separate file with the same root name, but with the extension “.LBL”.  The label file is stored in the same directory as the FITS data file that it describes.  The contents of the PDS label file are derived in part from the FITS header information contained in the HDU headers of the data file itself.

The data files themselves do not contain any embedded PDS headers, but do contain FITS headers according to the FITS standard [8].

An example of a LAMP EDR PDS label is found in Appendix E to this document.  An example of the FITS header is given in Appendix A.

# Applicable Software

The format of the LAMP EDR data product is standard FITS.  There are a number of different software libraries available that enable the reading and writing of standard FITS files.  These libraries are written in a number of different languages and are available for a variety of different computing platforms.  A list of these libraries can be found at the FITS Support Office web site (http://fits.gsfc.nasa.gov/).  Commonly used FITS libraries include the IDL Astronomy Library (http://idlastro.gsfc.nasa.gov/fitsio.html) and the CFITSIO/FITSIO library (http://heasarc.gsfc.nasa.gov/docs/software/fitsio/fitsio.html).  For this reason, no additional special software will be included in the EDR archive to parse and interpret the data files.

## Utility Programs

No utility programs are planned at this time.  However, they may be included in future revisions.

## Applicable PDS Software Tools

PDS archive products should be able to be displayed with the program NASAVIEW, developed by the PDS and available free of charge for a variety of computer platforms from the PDS web site (http://pds.jpl.nasa.gov/tools/software_download.cfm).

## Software Distribution and Update Procedures

Any developed software specific to LAMP EDR data products will be distributed with the EDR archive.  Version numbers and a CHANGELOG document will describe updates.  At this time, however, no need for any such software is anticipated.

# Appendix A – Detailed LAMP EDR FITS File Specifications

For each of the FITS HDUs described in Section 4.2 of this document, this Appendix lists and describes the specific header keywords and provides details on the format and layout of the data. Values followed by an asterisk (*) are variable on a per-file basis and are examples only.

| FITS Header Keyword | Value | Description |
| --- | --- | --- |
| FITS File Header | Primary HDU |  |
| SIMPLE | T | conforms to FITS standard |
| BITPIX | 32 | array data type |
| NAXIS | 2 | number of array dimensions |
| NAXIS1 | 1024 | number of spectral channels |
| NAXIS2 | 32 | number of spatial channels |
| EXTEND | T | FITS extensions present |
| BZERO | 0 | no offset |
| BSCALE | 1 | default scaling factor |
| COMMENT | Mission Data |  |
| MISSION | 'LRO' | Mission: Lunar Reconnaissance Orbiter |
| HOSTNAME | 'LRO' | Host name (PDS terminology) |
| INSTRUME | 'LAMP' | Instrument: Lyman Alpha Mapping Project |
| FILETIME | '2008-02-14T19:12:46' (*) | Time file was created by SOC |
| SL1PROC | 'LAMP-LIMA' | SOC pipeline level 1 software |
| SL1VER | ‘0.08’ | SOC pipeline level 1 software version |
| SL1DATE | '2008-02-14’ | SOC pipeline level 1 software date |
| TARGET | 'MOON' | Target object |
| ORIGIN | ‘SwRI’ | Southwest Research Institute (R) |
| COMMENT | Input (Source) Data |  |
| HKFILNAM | ‘LAMP000028.hk’ (*) | HK data file name/ident, from HK data file header, empty if none |
| HKSTRSEC | 223940575.900 (*) | HK data file start time (SCUT, sec) |
| HKENDSEC | 223940846.375 (*) | HK data file stop time (SCUT, sec) |
| HKSTRTIM | '2008-02-05T21:42:55.900' (*) | HK data file start time (UTC) |
| HKENDTIM | '2008-02-05T21:47:26.375' (*) | HK data file stop time (UTC) |
| SCFILNAM | ‘LAMP000028.sci’ (*) | Sci data file name/ident, from Science data file header, empty if none |
| SCSTRSEC | 223940575.900 (*) | Sci data file start time (SCUT, sec) |
| SCENDSEC | 223940846.375 (*) | Sci data file stop time (SCUT, sec) |
| SCSTRTIM | '2008-02-05T21:42:55.900' (*) | Sci data file start time (UTC) |
| SCENDTIM | '2008-02-05T21:47:26.375' (*) | Sci data file stop time (UTC) |
| PIXONLY | True/False | Flag indicating science file with only pixellist data |
| HISONLY | True/False | Flag indicating science file with only histogram data |
| COMMENT | General Hk Overview |  |
| PACKETS | 270 (*) | Total number of housekeeping packets |
| HKGAPS | True/False | Gaps in HK packet stream |
| HWVERS | FM, LIIS-1, LIIS-2 | Instrument H/W version/platform |
| SWVERS | 1.00 | Instrument flight software version |
| SWCHECK | ‘0xefd6’ | Instrument flight software checksum |
| LVPSSTAT | A / B / Both | LVPS status |
| TEMPSFTY | Active, None | Temperature Safety |
| ANODSFTY | Active, None | Anode Safety |
| STRPSFTY | Active, None | Strip Safety |
| HVSFTY | Active, None | HV Safety |
| BRTSFTY | Active, None | Bright Safety |
| CYCLSFTY | Active, None | Cycle Safety |
| LASTSFTY | Last Safety Temp, Anode, Strip, HV, Bright, Cycle, none | Last active safety |
| HACKCLCK | 0.004000118522 (*) | Instrument actual hack clock |
| HACKOFFS | 223940340.338 (*) | Instrument hack clock offset |
| HACKCORR | 0.953617 (*) | Instrument hack clock correlation |
| COMMENT | HVPS Hk Overview |  |
| HVPSSTAT | A / B / Both / None | HVPS status |
| HVLTSCTL | Day / Night / Var | HVPS LTS control |
| HVSETMIN | -4.946 (*) | Maximum HV set voltage (kVolt) |
| HVSETMAX | -4.946 (*) | Minimum HV set voltage (kVolt) |
| MCPV1MIN | -4.949 (*) | Maximum MCP Voltage 1 (kVolt) |
| MCPV1MAX | -4.949 (*) | Minimum MCP Voltage 1 (kVolt) |
| STPI1MIN | 14.30 (*) | Minimum Strip Current 1 (uA) |
| STPI1MAX | 14.30 (*) | Maximum Strip Current 1 (uA) |
| ANOV1MIN | -608 (*) | Maximum Anode Voltage 1 (kVolt) |
| ANOV1MAX | -605 (*) | Minimum Anode Voltage 1 (kVolt) |
| MCPV2MIN | -4.978 (*) | Maximum MCP Voltage 2 (kVolt) |
| MCPV2MAX | -4.978 (*) | Minimum MCP Voltage 2 (kVolt) |
| STPI2MIN | 3.78 (*) | Minimum Strip Voltage 2 (uA) |
| STPI2MAX | 3.90 (*) | Maximum Strip Voltage 2 (uA) |
| ANOV2MIN | -605 (*) | Maximum Anode Voltage 2 (kVolt) |
| ANOV2MAX | -605 (*) | Minimum Anode Voltage 2 (kVolt) |
| HVOPSLVL | -4.946 (*) | Operational HV Level (kVolt) |
| COMMENT | Detector Hk Overview |  |
| MINDISC | 1.05 (*) | minimum discriminator voltage (Volt) |
| MAXDISC | 1.05 (*) | maximum discriminator voltage (Volt) |
| EVCNTLO | 9588447 (*) | Lowest value of 24-bit HW event counter |
| EVCNTHI | 11374542 (*) | Highest value of 24-bit HW event counter |
| EVCOUNTS | 1792896 (*) | Total event counts during the orbit (mod 224) |
| MINCNTR | 6419 (*) | minimum countrate (Hz) |
| AVRCNTR | 6640.4 (*) | average countrate (Hz) |
| MAXCNTR | 6862 (*) | maximum countrate (Hz) |
| APDOOR | open / close / variable | Aperture door status during whole orbit |
| COMMENT | Temperature Hk Status |  |
| MINCDHT | 25.6 (*) | minimum C&DH temperature (degC) |
| AVRCDHT | 25.6 (*) | average C&DH temperature (degC) |
| MAXCDHT | 25.6 (*) | maximum C&DH temperature (degC) |
| MINDETHT | 22.3 (*) | minimum detector temperature (degC) |
| AVRDETHT | 22.3 (*) | average detector temperature (degC) |
| MAXDETHT | 22.3 (*) | maximum detector temperature (degC) |
| MINMIRAT | 22.7 (*) | minimum Mirror A temperature (degC) |
| AVRMIRAT | 22.7 (*) | average Mirror A temperature (degC) |
| MAXMIRAT | 22.7 (*) | maximum Mirror A temperature (degC) |
| MINMIRBT | 22.7 (*) | minimum Mirror B temperature (degC) |
| AVRMIRBT | 22.7 (*) | average Mirror B temperature (degC) |
| MAXMIRBT | 22.7 (*) | maximum Mirror B temperature (degC) |
| MINGRTAT | 21.6 (*) | minimum Grating A temperature (degC) |
| AVRGRTAT | 21.6 (*) | average Grating A temperature (degC) |
| MAXGRTAT | 21.6 (*) | maximum Grating A temp (degC) |
| MINGRTBT | 21.6 (*) | minimum Grating B temperature (degC) |
| AVRGRTBT | 21.6 (*) | average Grating B temperature (degC) |
| MAXGRTBT | 21.6 (*) | maximum Grating B temp (degC) |
| MIRHTRST | On, Off, Variable | Mirror heaters status |
| GRTHTRST | On, Off, Variable | Grating heaters status |
| DETDOOR | Open, Close, Variable | Detector door status |
| COMMENT | Spectral Image Door open status |  |
| DOEVTN | 1215913 (*) | Door Open events in the histogram |
| DOTIME | 199.974 (*) | Total Door Open time (sec) |
| DOSOURCE | ‘histo’ / ‘ground’ | Source of the histogram information Histogram (on-board) or Ground (Pixellist) |
| DOMAXCNT | 10235 (*) | Maximum count in the door open histogram |
| DOMINCNT | 0 (*) | Minimum count in the door open histogram |
| DOMAXCR | 6862 (*) | Door open histogram maximum countrate (Hz) |
| DOMINCR | 6419 (*) | Door open histogram minimum countrate (Hz) |
| DOPATTRN | data, inc hi, inc lo, dec hi, dec lo, const | Data or test pattern in the door open histogram dataset |
| DOLTS | Day, Night, Var | Door open histogram LTS status |
| DOSTIMS | Off, Stim, Var | STIM status for the door open dataset |
| DOHVPS | A, B, Both, None, Variable | HVPS commanded status for the door open dataset |
| END |  |  |
| Primary HDU Data | Spectral Image Door Open | 2-D array 1024x32 of 32 bit event counts |
| XTENSION | ‘IMAGE’ | Extension 1, Spectral Image Door Closed |
| BITPIX | 32 | array data type, 32 bit words |
| NAXIS | 2 | number of array dimensions |
| NAXIS1 | 1024 | number of spectral channels |
| NAXIS2 | 32 | number of spatial channels |
| BZERO | 0 | no offset |
| BSCALE | 1 | default scaling factor |
| PCOUNT | 0 | extension size parameter |
| GCOUNT | 1 | extension size parameter |
| EXTNAME | ‘Door Closed Histogram’ | Extension name |
| EXTVER | 1 | Extension version number |
| COMMENT | Spectral Image Door closed status |  |
| DCEVTN | 0 (*) | Door closed events in the histogram |
| DCTIME | 0.000 (*) | Total Door closed acquisition time (sec) |
| DCSOURCE | HISTO / GROUND | Source of the histogram information Histogram (on-board) or Ground (Pixellist) |
| DCMAXCNT | 0 (*) | Maximum count in door closed histogram |
| DCMINCNT | 0 (*) | Minimum count in door closed histogram |
| DCMAXCR | 0 (*) | Door closed histogram maximum countrate (Hz) |
| DCMINCR | -1 (*) | Door closed histogram minimum countrate (Hz) |
| DCPATTRN | data, inc hi, inc lo, dec hi, dec lo, const | Data or test pattern in the door open histogram dataset |
| DCLTS | Day, Night, Var | Door closed histogram LTS status |
| DCSTIMS | ON, OFF, Variable | STIM status for the door open dataset |
| DCHVPS | A, B, Both, None, Variable | HVPS commanded status for the door open dataset |
| END |  |  |
| Extension 1 HDU Data | Spectral Image Door Closed | 1024 x 32 array of 32 bit event counts |
| XTENSION | ‘TABLE’ | Extension 2, Acquisition List |
| BITPIX | 8 | array data type, 8-bit ASCII characters |
| NAXIS | 2 | number of array dimensions |
| NAXIS1 | 64 | number of characters per line |
| NAXIS2 | 38 (*) | number of acquisitions |
| PCOUNT | 0 | extension size parameter |
| GCOUNT | 1 | extension size parameter |
| TFIELDS | 12 | Number of element fields per line |
| EXTNAME | ‘Acquisition List (HK)’ | Acquisition/frames list |
| EXTVER | 1 | Extension version number |
| TFORM1 | ‘D14.3’ | Format of field 1 |
| TFORM2 | ‘D14.3’ | Format of field 2 |
| TFORM3 | ‘I5’ | Format of field 3 |
| TFORM4 | ‘I1’ | Format of field 4 |
| TFORM5 | ‘I4’ | Format of field 5 |
| TFORM6 | ‘I1’ | Format of field 6 |
| TFORM7 | ‘I1’ | Format of field 7 |
| TFORM8 | ‘I1’ | Format of field 8 |
| TFORM9 | ‘I1’ | Format of field 9 |
| TFORM10 | ‘I1’ | Format of field 10 |
| TFORM11 | ‘I2’ | Format of field 11 |
| TFORM12 | ‘I8’ | Format of field 12 |
| TBCOL1 | 1 | Start column for field 1 |
| TBCOL2 | 16 | Start column for field 2 |
| TBCOL3 | 31 | Start column for field 3 |
| TBCOL4 | 37 | Start column for field 4 |
| TBCOL5 | 39 | Start column for field 5 |
| TBCOL6 | 44 | Start column for field 6 |
| TBCOL7 | 46 | Start column for field 7 |
| TBCOL8 | 48 | Start column for field 8 |
| TBCOL9 | 50 | Start column for field 9 |
| TBCOL10 | 52 | Start column for field 10 |
| TBCOL11 | 54 | Start column for field 11 |
| TBCOL12 | 57 | Start column for field 12 |
| TTYPE1 | ‘START_TIME’ | Start time of acquisition (sec since 1/1/2001) |
| TTYPE2 | ‘STOP_TIME’ | Stop time of acquisition (sec since 1/1/2001) |
| TTYPE3 | ‘SCI_HDR’ | Science frame header from HK stream |
| TTYPE4 | ‘ACQ_MODE’ | Acquisition type (0=pixel, 1=histo) |
| TTYPE5 | ‘FRAME_NO’ | Frame number (0-4095) |
| TTYPE6 | ‘APD_STATE’ | Aperture door state (1=error, 2=closed, 3=open, 4=between, 5=variable) |
| TTYPE7 | ‘LTS_STATE’ | LTS state (1=day, 2=dark, 5=variable) |
| TTYPE8 | ‘STIM_STATE’ | STIM state (1=off, 2=on, 5=variable) |
| TTYPE9 | ‘HVPS_STATE’ | HVPS state (1=off, 2=A, 3=B, 4=both, 5=variable) |
| TTYPE10 | ‘HACK_RATE’ | Hack rate (0=N/A, 1=4 msec, 2=8 msec, …, 8=512 msec) |
| TTYPE11 | ‘FR_PATTERN’ | Data pattern (0=data, 1=no frame, 2=test pattern) |
| TTYPE12 | ‘CHECKSUM’ | Frame data checksum (3 bytes) |
| TUNIT1 | ‘sec’ | Unit for SCUT |
| TUNIT2 | ‘sec’ | Unit for SCUT |
| COMMENT |  |  |
| NHKACQS | 38 (*) | number of acquisitions reported in housekeeping data |
| CONACQS | True / False | true if all the acquisitions in this extension are continuous |
| FACQSTA | 223940640.795 (*) | first acquisition start time |
| LACQEND | 223940840.795 (*) | last acquisition end time |
| PIXONLY | true / false | pixellist acquistions only in this file |
| HISONLY | true / false | histogram acquisitions only in this file |
| END |  |  |
| Extension 2 HDU Data | Acquisition List | ASCII Data Table with number of entries matching number of acquisitions, empty if no acquisitions reported in housekeeping data |
| XTENSION | ‘BINTABLE’ | Extension 3, Frame Data |
| BITPIX | 8 | array data type, 8-bit bytes |
| NAXIS | 2 | number of array dimensions |
| NAXIS1 | 65544 | number of bytes per frame |
| NAXIS2 | 38 (*) | number of science frames |
| PCOUNT | 0 | extension size parameter |
| GCOUNT | 1 | extension size parameter |
| TFIELDS | 2 | Number of element fields per line |
| EXTNAME | ‘Raw Science Frame Data (SCI)’ | Extension name |
| EXTVER | 1 | Extension version number |
| TTYPE1 | ‘GEN_TIME’ | Frame generation time |
| TTYPE2 | ‘FRAME_DATA’ | Raw frame data |
| TFORM1 | ‘D’ | Column 1 format |
| TFORM2 | ‘32768I’ | Column 2 format |
| TZERO2 | 32768 | Zero offset to get unsigned integers |
| TDISP1 | ‘D14.3’ | Preferred display format for SCUT |
| TUNIT1 | ‘sec’ | Unit for SCUT |
| COMMENT |  |  |
| NFRAMES | 38 (*) | number of science frames |
| FRMONE | 18 (*) | first frame number |
| FRMLAST | 55 (*) | last frame number |
| CONTFRM | True / False | continuous frame sequence flag |
| FRMDATA | ‘histo’ / ‘pixel’ / ‘mixed’ | Frame data type |
| END |  |  |
| Extension 3 HDU Data | Frame Data | Linear list of 16 bit words with length a multiple of 32768+3 words |
| XTENSION | ‘BINTABLE’ | Extension 4, Calculated countrate |
| BITPIX | 8 | array data type, 8-bit bytes |
| NAXIS | 2 | number of array dimensions |
| NAXIS1 | 16 | Number of bytes per countrate entry |
| NAXIS2 | 12498 (*) | Number of countrate entries |
| PCOUNT | 0 | extension size parameter |
| GCOUNT | 1 | extension size parameter |
| TFIELDS | 3 | Number of element fields per line |
| EXTNAME | ‘Calculated Countrate (SCI)’ | Extension name |
| EXTVER | 1 | Extension version number |
| TTYPE1 | ‘HACK_TIME’ | Hack time at interval start (wrap extended) |
| TTYPE2 | ‘SCUT_TIME’ | Hack time converted to SCUT (sec) |
| TTYPE3 | ‘COUNT_RATE’ | Countrate for the interval (Hz) |
| TFORM1 | ’J’ | 4 byte long |
| TFORM2 | ’D’ | 8 byte double |
| TFORM3 | ’J’ | 4 byte long |
| TDISP2 | ’D14.3’ | Preferred display format for SCUT |
| TUNIT2 | ’sec’ | Unit for SCUT |
| TUNIT3 | ’Hz’ | Unit for countrate |
| COMMENT |  |  |
| CRTIME | 199.974 (*) | Time span for countrate data |
| MINCR | 4124 (*) | Overall minimum countrate (Hz) |
| AVRCR | 6164.0 (*) | Overall average countrate (Hz) |
| MAXCR | 8312 (*) | Overall maximum countrate (Hz) |
| MINCRDO | 4124 (*) | Door open minimum countrate (Hz) |
| AVRCRDO | 6080.4 (*) | Door open average countrate (Hz) |
| MAXCRDO | 8312 (*) | Door open maximum countrate (Hz) |
| MINCRDC | 65535 (*) | Door closed minimum countrate (Hz) |
| AVRCRDC | -1.0 (*) | Door closed average countrate (Hz) |
| MAXCRDC | 0 (*) | Door closed maximum countrate (Hz) |
| END |  |  |
| Extension 4 HDU Data | Calculated countrate | Binary data table with 1 value per entry, each representing a countrate in Hz |
| XTENSION | ‘BINTABLE’ | Extension 5, LTS data |
| BITPIX | 8 | array data type, 8-bit bytes |
| NAXIS | 2 | number of array dimensions |
| NAXIS1 | 14 | Number of bytes per table row |
| NAXIS2 | 2700 (*) | Number of LTS entries |
| PCOUNT | 0 | extension size parameter |
| GCOUNT | 1 | extension size parameter |
| TFIELDS | 4 | Number of element fields per line |
| EXTNAME | ‘LTS Data (HK)’ | Extension name |
| EXTVER | 1 | Extension version number |
| TTYPE1 | ’HACK_TIME’ | Hack time at interval start (wrap extended) |
| TTYPE2 | ‘SCUT_TIME’ | Hack time converted to SCUT (sec) |
| TTYPE3 | ‘LTS_A’ | LTS A high rate scaled value |
| TTYPE4 | ‘LTS_B’ | LTS B high rate scaled value |
| TFORM1 | ‘J’ | 4 byte long |
| TFORM2 | ‘D’ | 8 byte double |
| TFORM3 | ‘B’ | One byte |
| TFORM4 | ‘B’ | One byte |
| TDISP2 | ‘D14.3’ | Preferred display format for time |
| TUNIT2 | ‘sec’ | Unit for SCUT |
| COMMENT |  |  |
| LTSAVALD | True / False | LTS A data valid flag |
| LTSBVALD | True / False | LTS B data valid flag |
| LTSTVALD | True / False | LTS timing data valid flag |
| LTSAMIN | 121 (*) | LTS A minimum value |
| LTSAAVR | 166.0 (*) | LTS A average value |
| LTSAMAX | 214 (*) | LTS A maximum value |
| LTSBMIN | 69 (*) | LTS B minimum value |
| LTSBAVR | 84.2 (*) | LTS B average value |
| LTSBMAX | 108 (*) | LTS B maximum value |
| END |  |  |
| Extension 5 HDU Data | LTS data | Data table with 3 values per entry, some columns may be empty, length is equal to number of housekeeping packets times ten |
| XTENSION | ‘BINTABLE’ | Extension 6, Housekeeping Table |
| BITPIX | 8 | array data type, 8-bit bytes |
| NAXIS | 2 | number of array dimensions |
| NAXIS1 | 229 | Bytes needed to encode one LAMP HK packet, plus calibrated raw values |
| NAXIS2 | 270 (*) | Number of housekeeping packets |
| PCOUNT | 0 | extension size parameter |
| GCOUNT | 1 | extension size parameter |
| TFIELDS | 37 | Number of element fields per line |
| EXTNAME | ‘Housekeeping Table (HK)’ | Extension name |
| EXTVER | 1 | Extension version number |
| TTYPE1 | ‘SCUT_TIME’ | Spacecraft UTC (sec since epoch from HK) |
| TTYPE2 | ‘HACK_TIME’ | Extended instrument hack time (since HK on) |
| TTYPE3 | ‘PACK_CNT’ | 14-bit packet count (since HK on) |
| TTYPE4 | ‘PACKET_DATA’ | Raw HK CCSDS packet (122 bytes) |
| TTYPE5 | ‘INST_STATE’ | Instrument state (2,6=SAFE, 1,5=CHK, 3=PIX, 7=HIS) |
| TTYPE6 | ‘LAST_SAFETY’ | Last safety (0=none) |
| TTYPE7 | ‘LVPS_STAT’ | Active LVPS (1=A, 2=B, 3=both) |
| TTYPE8 | ‘HVPS_STAT’ | Active HVPS (0=off, 1=A, 2=B, 3=both) |
| TTYPE9 | ‘MIRR_TMP_SET’ | Mirror temperature set point (degC) |
| TTYPE10 | ‘GRAT_TMP_SET’ | Grating temperature set point (degC) |
| TTYPE11 | ‘MIRR_HTR_STAT’ | Mirror heater status (0=off, 1=A, 2=B, 3=both) |
| TTYPE12 | ‘GRAT_HTR_STAT’ | Grating heater status (0=off, 1=A, 2=B, 3=both) |
| TTYPE13 | ‘MIRR_A_TMP’ | Mirror temperature A (primary) (degC) |
| TTYPE14 | ‘MIRR_B_TMP’ | Mirror temperature B (redundant) (degC) |
| TTYPE15 | ‘GRAT_A_TMP’ | Grating temperature A (primary) (degC) |
| TTYPE16 | ‘GRAT_B_TMP’ | Grating temperature B (redundant) (degC) |
| TTYPE17 | ‘CDH_ELEC_TMP’ | C&DH electronics temperature (degC) |
| TTYPE18 | ‘DET_HOUS_TMP’ | Detector housing temperature (degC) |
| TTYPE19 | ‘APDOOR’ | Aperture door (1=closed, 2=open, 3=between) |
| TTYPE20 | ‘LTS_DARK’ | LTS dark status (0=light, 1=dark) |
| TTYPE21 | ‘STIM_STAT’ | STIM status (0=off, 1=on) |
| TTYPE22 | ‘HV_SETPNT’ | Detector HVPS setpoint (kVolt) |
| TTYPE23 | ‘MCPV1’ | Detector MCP voltage 1 (kVolt) |
| TTYPE24 | ‘ANODEV1’ | Detector anode voltage 1 (kVolt) |
| TTYPE25 | ‘STRIPI1’ | Detector strip current 1 (uA) |
| TTYPE26 | ‘MCPV2’ | Detector MCP voltage 2 (kVolt) |
| TTYPE27 | ‘ANODEV2’ | Detector anode voltage 2 (kVolt) |
| TTYPE28 | ‘STRIPI2’ | Detector strip current 2 (uA) |
| TTYPE29 | ‘MAX_MCPV’ | Maximum MCP voltage last second (kVolt) |
| TTYPE30 | ‘MAX_STRIPI’ | Maximum summed strip current last second (uA) |
| TTYPE31 | ‘DISCRIM’ | Detector discriminator voltage (Volt) |
| TTYPE32 | ‘COUNT_RATE’ | Analog (raw) countrate (Hz) |
| TTYPE33 | ‘RAW_LTS_A’ | Raw LTS A (14 bits, raw counts) |
| TTYPE34 | ‘RAW_LTS_B’ | Raw LTS B (14 bits, raw counts) |
| TTYPE35 | ‘LTS_CYCLES’ | LTS safing cycles in acquisition |
| TTYPE36 | ‘SAFETY’ | Current safety status (0=none pending) |
| TTYPE37 | ‘SAFE_TIMER’ | Safety timeout timer (sec remaining) |
| TFORM1 | ‘D’ | 8 byte double |
| TFORM2 | ‘J’ | 4 byte long |
| TFORM3 | ‘I’ | 2 byte integer |
| TFORM4 | ‘122B’ | 122 bytes |
| TFORM5 | ‘B’ | 1 byte state |
| TFORM6 | ‘B’ | 1 byte state |
| TFORM7 | ‘B’ | 1 byte state |
| TFORM8 | ‘B’ | 1 byte state |
| TFORM9 | ‘E’ | 4 byte float |
| TFORM10 | ‘E’ | 4 byte float |
| TFORM11 | ‘B’ | 1 byte state |
| TFORM12 | ‘B’ | 1 byte state |
| TFORM13 | ‘E’ | 4 byte float |
| TFORM14 | ‘E’ | 4 byte float |
| TFORM15 | ‘E’ | 4 byte float |
| TFORM16 | ‘E’ | 4 byte float |
| TFORM17 | ‘E’ | 4 byte float |
| TFORM18 | ‘E’ | 4 byte float |
| TFORM19 | ‘B’ | 1 byte state |
| TFORM20 | ‘B’ | 1 byte state |
| TFORM21 | ‘B’ | 1 byte state |
| TFORM22 | ‘E’ | 4 byte float |
| TFORM23 | ‘E’ | 4 byte float |
| TFORM24 | ‘E’ | 4 byte float |
| TFORM25 | ‘E’ | 4 byte float |
| TFORM26 | ‘E’ | 4 byte float |
| TFORM27 | ‘E’ | 4 byte float |
| TFORM28 | ‘E’ | 4 byte float |
| TFORM29 | ‘E’ | 4 byte float |
| TFORM30 | ‘E’ | 4 byte float |
| TFORM31 | ‘E’ | 4 byte float |
| TFORM32 | ‘J’ | 4 byte long |
| TFORM33 | ‘I’ | 2 byte integer |
| TFORM34 | ‘I’ | 2 byte integer |
| TFORM35 | ‘B’ | 1 byte integer |
| TFORM36 | ‘B’ | 1 byte status |
| TFORM37 | ‘I’ | 2 byte integer |
| COMMENT |  |  |
| TDISP1 | ‘D14.3’ | Preferred display format for time |
| TUNIT1 | ‘sec’ | Unit for time |
| TUNIT2 | ‘hacks’ | Unit for time |
| TDISP9 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT9 | ‘degC’ | Unit for temperature |
| TDISP10 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT10 | ‘degC’ | Unit for temperature |
| TDISP13 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT13 | ‘degC’ | Unit for temperature |
| TDISP14 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT14 | ‘degC’ | Unit for temperature |
| TDISP15 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT15 | ‘degC’ | Unit for temperature |
| TDISP16 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT16 | ‘degC’ | Unit for temperature |
| TDISP17 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT17 | ‘degC’ | Unit for temperature |
| TDISP18 | ‘F5.1’ | Preferred display format for temperature |
| TUNIT18 | ‘degC’ | Unit for temperature |
| TDISP22 | ‘F6.3’ | Preferred display unit for HvSet |
| TUNIT22 | ‘kVolt’ | Unit for HvSet |
| TDISP23 | ‘F6.3’ | Preferred display unit for McpV |
| TUNIT23 | ‘kVolt’ | Unit for McpV |
| TDISP24 | ‘F4.1’ | Preferred display format for AnodeV |
| TUNIT24 | ‘Volt’ | Unit for AnodeV |
| TDISP25 | ‘F5.2’ | Preferred display format for Strip Current |
| TUNIT25 | ‘uA’ | Unit for Strip Current |
| TDISP26 | ‘F6.3’ | Preferred display unit for McpV |
| TUNIT26 | ‘kVolt’ | Unit for McpV |
| TDISP27 | ‘F4.1’ | Preferred display format for AnodeV |
| TUNIT27 | ‘Volt’ | Unit for AnodeV |
| TDISP28 | ‘F5.2’ | Preferred display format for Strip Current |
| TUNIT28 | ‘uA’ | Unit for Strip Current |
| TDISP29 | ‘F6.3’ | Preferred display unit for McpV |
| TUNIT29 | ‘kVolt’ | Unit for McpV |
| TDISP30 | ‘F5.2’ | Preferred display format for Strip Current |
| TUNIT30 | ‘uA’ | Unit for Strip Current |
| TDISP31 | ‘F4.2’ | Preferred display format for Discriminator |
| TUNIT31 | ‘Volt’ | Unit for Discriminator |
| TUNIT32 | ‘Hz’ | Unit for Countrate |
| TUNIT33 | ‘counts’ | Unit for raw LTS |
| TUNIT34 | ‘counts’ | Unit for raw LTS |
| TUNIT37 | ‘sec’ | Unit for safety timeout |
| COMMENT |  |  |
| HKEARLY | 223940576.795 (*) | Earliest HK packet time (after sync) |
| HKLATEST | 223940845.795 (*) | Latest HK packet time |
| HKENTRS | 270 (*) | total number of HK packets |
| COMPHK | True / False | complete list flag (after sync) |
| ORDRHK | True / False | incrementing time order flag |
| END |  |  |
| Extension 6: | Housekeeping Table | HK data table, including both the raw values and the values converted into engineering units where applicable. |

# Appendix B – Glossary

Archive – An archive consists of one or more data sets along with all the documentation and ancillary information needed to understand and use the data. An archive is a logical construct independent of the medium on which it is stored.

Archive Volume, Archive Volume Set – A volume is a unit of media on which data products are stored; for example, one CD-ROM or DVD-ROM. An archive volume is a volume containing all or part of an archive; that is, data products plus documentation and ancillary files. When an archive spans multiple volumes, they are called an archive volume set. Usually the documentation and some ancillary files are repeated on each volume of the set, so that a single volume can be used alone.

Catalog Information – Descriptive information about a data set (e.g. mission description, spacecraft description, instrument description), expressed in Object Description Language (ODL) which is suitable for loading into a PDS catalog.

Data Product – A labeled grouping of data resulting from a scientific observation, usually stored in one file. A product label identifies, describes, and defines the structure of the data. An example of a data product is a planetary image, a spectrum table, or a time series table.

Data Set – An accumulation of data products. A data set together with supporting documentation and ancillary files is an archive.

Standard Data Product – A data product generated in a predefined way using well-understood procedures, processed in "pipeline" fashion. Data products that are generated in a nonstandard way are sometimes called special data products.

# Appendix C – Acronyms and Abbreviations

| ASCII | American Standard Code for Information Interchange |
| --- | --- |
| C&DH | Command and Data Handling |
| CD-ROM | Compact Disk - Read-Only Memory |
| CODMAC | Committee on Data Management, Archiving and Computing |
| DVD-ROM | Digital Video Disk – Read-Only Memory |
| EDR | Experiment Data Record |
| FITS | Flexible Image Transport System |
| HDU | Header and Data Unit (FITS) |
| HK | Housekeeping |
| HVPS | High-Voltage Power Supply |
| HW | Hardware |
| IAU | International Astronomical Union |
| ICD | Interface Control Document |
| IDL | Interactive Data Language |
| ISO | International Standards Organization |
| JPL | Jet Propulsion Laboratory |
| LAMP | Lyman Alpha Mapping Project |
| LRO | Lunar Reconnaissance Orbiter |
| LTS | Lunar Terminator Sensor |
| MCP | Microchannel Plate |
| MOC | Mission Operations Center |
| MSB | Most Significant Bit |
| NAIF | Navigation and Ancillary Information Facility |
| NASA | National Aeronautics and Space Administration |
| PDS | Planetary Data System |
| SCLK | Spacecraft Clock (SPICE kernel) |
| SCUT | Spacecraft Universal Time |
| SIS | Software Interface Specification |
| SOC | Science Operations Center |
| SPICE | Spacecraft, Planet, Instrument, C-matrix (pointing), and Events |
| TBD | To Be Determined |
| TBS | To Be Supplied |
| UTC | Coordinated Universal Time |
| UV | Ultraviolet |

# Appendix D – NASA and CODMAC Data Level Definitions

| NASA | CODMAC | Description |
| --- | --- | --- |
| Packet data | Raw - Level 1 | Telemetry data stream as received at the ground station, with science and engineering data embedded. |
| Level 0 | Edited - Level 2 | Instrument science data (e.g., raw voltages, counts) at full resolution, time ordered, with duplicates and transmission errors removed. |
| Level 1A | Calibrated - Level 3 | NASA Level 0 data that have been located in space and may have been transformed (e.g., calibrated, rearranged) in a reversible manner and packaged with needed ancillary and auxiliary data (e.g., radiances with the calibration equations applied). |
| Level 1B | Resampled - Level 4 | Irreversibly transformed (e.g., resampled, remapped, calibrated) values of the instrument measurements (e.g., radiances, magnetic field strength). |
| Level 1C | Derived - Level 5 | NASA Level 1A or 1B data that have been resampled and mapped onto uniform space-time grids. The data are calibrated (i.e., radiometrically corrected) and may have additional corrections applied (e.g., terrain correction). |
| Level 2 | Derived - Level 5 | Geophysical parameters, generally derived from Level 1 data, and located in space and time commensurate with instrument location, pointing, and sampling. |
| Level 3 | Derived - Level 5 | Geophysical parameters mapped onto uniform space-time grids. |

# Appendix E – Example PDS Label

Below is an example PDS label for the LAMP EDR data product.

PDS_VERSION_ID                = PDS3

DD_VERSION_ID                 = PDSCAT1R65

LABEL_REVISION_NOTE           = "2008-02-15, David E. Kaufmann (SwRI), V0.1;"

/* FILE CHARACTERISTIC DATA ELEMENTS */

DATA_FORMAT                   = FITS

FILE_NAME                     = "LAMP_ENG_0223940575_00.FIT"

FILE_RECORDS                  = 1078

RECORD_BYTES                  = 2880 /* FITS standard record length */

RECORD_TYPE                   = FIXED_LENGTH

/* DATA OBJECT POINTERS */

^SPECTRAL_IMAGE_DOOR_OPEN_HEADER   = ("LAMP_ENG_0223940575_00.FIT", 1)

^SPECTRAL_IMAGE_DOOR_OPEN_IMAGE    = ("LAMP_ENG_0223940575_00.FIT", 5)

^SPECTRAL_IMAGE_DOOR_CLOSED_HEADER = ("LAMP_ENG_0223940575_00.FIT", 51)

^SPECTRAL_IMAGE_DOOR_CLOSED_IMAGE  = ("LAMP_ENG_0223940575_00.FIT", 52)

^ACQUISITION_LIST_HEADER           = ("LAMP_ENG_0223940575_00.FIT", 98)

^ACQUISITION_LIST_TABLE            = ("LAMP_ENG_0223940575_00.FIT", 100)

^FRAME_DATA_HEADER                 = ("LAMP_ENG_0223940575_00.FIT", 101)

^FRAME_DATA_TABLE                  = ("LAMP_ENG_0223940575_00.FIT", 102)

^CALCULATED_COUNTRATE_HEADER       = ("LAMP_ENG_0223940575_00.FIT", 967)

^CALCULATED_COUNTRATE_TABLE        = ("LAMP_ENG_0223940575_00.FIT", 968)

^LTS_DATA_HEADER                   = ("LAMP_ENG_0223940575_00.FIT", 1038)

^LTS_DATA_TABLE                    = ("LAMP_ENG_0223940575_00.FIT", 1039)

^HOUSEKEEPING_HEADER               = ("LAMP_ENG_0223940575_00.FIT", 1053)

^HOUSEKEEPING_TABLE                = ("LAMP_ENG_0223940575_00.FIT", 1057)

/* IDENTIFICATION DATA ELEMENTS */

DATA_SET_ID                   = "LRO-L-LAMP-2-EDR-V1.0"

INSTRUMENT_HOST_NAME          = "LUNAR RECONNAISSANCE ORBITER"

INSTRUMENT_NAME               = "LYMAN ALPHA MAPPING PROJECT"

PRODUCT_CREATION_TIME         = 2008-02-14T19:12:46

PRODUCT_ID                    = "LAMP_ENG_0223940575_00.FIT"

SPACECRAFT_CLOCK_START_COUNT  = "223940575.900"

SPACECRAFT_CLOCK_STOP_COUNT   = "223940846.375"

START_TIME                    = 2008-02-05T21:42:55.900

STOP_TIME                     = 2008-02-05T21:47:26.375

TARGET_NAME                   = "MOON"

/* DESCRIPTIVE DATA ELEMENTS */

DATA_QUALITY_ID               = 0

DATA_QUALITY_DESC             = "Data quality is nominal"

DATA_SET_NAME                 = "LRO MOON LAMP 2 EXPERIMENT DATA RECORD V1.0"

EXPOSURE_DURATION             = 199.990 <s>

INSTRUMENT_HOST_ID            = "LRO"

INSTRUMENT_ID                 = "LAMP"

INSTRUMENT_MODE_ID            = "PIXEL" /* PIXEL, HISTO, MIXED */

INSTRUMENT_MODE_DESC          = "PIXELLIST"

INSTRUMENT_TYPE               = "SPECTROGRAPH"

MISSION_ID                    = "LRO"

MISSION_NAME                  = "LUNAR RECONNAISSANCE ORBITER"

MISSION_PHASE_NAME            = "PRIMARY MISSION"

PRODUCER_FULL_NAME            = "DAVID E. KAUFMANN"

PRODUCER_ID                   = "LRO_LAMP"

PRODUCER_INSTITUTION_NAME     = "SOUTHWEST RESEARCH INSTITUTE"

PRODUCT_TYPE                  = "EDR" /* CODMAC Data Level 2 */

SOFTWARE_NAME                 = "LAMP-LIMA"

SPACECRAFT_NAME               = "LUNAR RECONNAISSANCE ORBITER"

TARGET_DESC                   = "MOON"

TARGET_TYPE                   = "SATELLITE"

/* DATA OBJECT DEFINITIONS */

OBJECT                        = SPECTRAL_IMAGE_DOOR_OPEN_HEADER

BYTES                       = 11520 /* RECORD_BYTES x RECORDS */

HEADER_TYPE                 = FITS

INTERCHANGE_FORMAT          = ASCII

RECORDS                     = 4

DESCRIPTION                 = "

FITS header for LRO LAMP uncalibrated (CODMAC Data Level 2)

observation."

END_OBJECT                    = SPECTRAL_IMAGE_DOOR_OPEN_HEADER

OBJECT                        = SPECTRAL_IMAGE_DOOR_OPEN_IMAGE

SAMPLE_BITS                 = 32

SAMPLE_TYPE                 = MSB_INTEGER

AXIS_ORDER_TYPE             = FIRST_INDEX_FASTEST

LINE_DISPLAY_DIRECTION      = UP

SAMPLE_DISPLAY_DIRECTION    = RIGHT

LINE_SAMPLES                = 1024

LINES                       = 32

INTERCHANGE_FORMAT          = BINARY

OFFSET                      = 0

SCALING_FACTOR              = 1.00000

DESCRIPTION                 = "

Reconstructed histogram image for LRO LAMP uncalibrated (CODMAC

Data Level 2) pixel list data taken with the instrument aperture

door open, or first histogram image if all data taken in histogram

mode.  Units are raw data numbers."

END_OBJECT                    = SPECTRAL_IMAGE_DOOR_OPEN_IMAGE

OBJECT                        = SPECTRAL_IMAGE_DOOR_CLOSED_HEADER

BYTES                       = 2880 /* RECORD_BYTES x RECORDS */

HEADER_TYPE                 = FITS

INTERCHANGE_FORMAT          = ASCII

RECORDS                     = 1

DESCRIPTION                 = "

This is the FITS header for FITS extension number = 1, FITS

extension name = SPECTRAL_IMAGE_DOOR_CLOSED"

END_OBJECT                    = SPECTRAL_IMAGE_DOOR_CLOSED_HEADER

OBJECT                        = SPECTRAL_IMAGE_DOOR_CLOSED_IMAGE

SAMPLE_BITS                 = 32

SAMPLE_TYPE                 = MSB_INTEGER

AXIS_ORDER_TYPE             = FIRST_INDEX_FASTEST

LINE_DISPLAY_DIRECTION      = UP

SAMPLE_DISPLAY_DIRECTION    = RIGHT

LINE_SAMPLES                = 1024

LINES                       = 32

INTERCHANGE_FORMAT          = BINARY

OFFSET                      = 0

SCALING_FACTOR              = 1.00000

DESCRIPTION                 = "

Reconstructed histogram image for LRO LAMP uncalibrated (CODMAC

Data Level 2) pixel list data taken with the instrument aperture

door closed, or second histogram image if all data taken in

histogram mode.  Units are raw data numbers."

END_OBJECT                    = SPECTRAL_IMAGE_DOOR_CLOSED_IMAGE

OBJECT                        = ACQUISITION_LIST_HEADER

BYTES                       = 5760 /* RECORD_BYTES x RECORDS */

HEADER_TYPE                 = FITS

INTERCHANGE_FORMAT          = ASCII

RECORDS                     = 2

DESCRIPTION                 = "

This is the FITS header for FITS extension number = 2, FITS

extension name = ACQUISITION_LIST"

END_OBJECT                    = ACQUISITION_LIST_HEADER

OBJECT                        = ACQUISITION_LIST_TABLE

INTERCHANGE_FORMAT          = ASCII

ROWS                        = 38

COLUMNS                     = 12

ROW_BYTES                   = 64

OBJECT                      = COLUMN

NAME                      = "START_TIME"

DATA_TYPE                 = ASCII_REAL

START_BYTE                = 1

BYTES                     = 15

DESCRIPTION               = "

Start time of acquisition (seconds since 00:00 UTC, 01 Jan 2001)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "STOP_TIME"

DATA_TYPE                 = ASCII_REAL

START_BYTE                = 16

BYTES                     = 15

DESCRIPTION               = "

Stop time of acquisition (seconds since 00:00 UTC, 01 Jan 2001)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "SCI_HDR"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 31

BYTES                     = 6

DESCRIPTION               = "

Science frame header from HK stream"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "ACQ_MODE"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 37

BYTES                     = 2

DESCRIPTION               = "

Acquisition type (0=pixellist, 1=histogram)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "FRAME_NO"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 39

BYTES                     = 5

DESCRIPTION               = "

Frame number (0-4095)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "APD_STATE"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 44

BYTES                     = 2

DESCRIPTION               = "

Aperture door state (1=error, 2=closed, 3=open, 4=between,

5=variable)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "LTS_STATE"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 46

BYTES                     = 2

DESCRIPTION               = "

LTS state (1=day, 2=dark, 5=variable)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "STIM_STATE"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 48

BYTES                     = 2

DESCRIPTION               = "

STIM state (1=off, 2=on, 5=variable)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "HVPS_STATE"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 50

BYTES                     = 2

DESCRIPTION               = "

HVPS state (1=off, 2=A, 3=B, 4=both, 5=variable)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "HACK_RATE"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 52

BYTES                     = 2

DESCRIPTION               = "

Hack rate (0=N/A, 1=4 msec, 2=8 msec, ..., 8=512 msec)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "FR_PATTERN"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 54

BYTES                     = 3

DESCRIPTION               = "

Data pattern (0=data, 1=no frame, 2=test pattern)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "CHECKSUM"

DATA_TYPE                 = ASCII_INTEGER

START_BYTE                = 57

BYTES                     = 8

DESCRIPTION               = "

Frame data checksum (3 bytes)"

END_OBJECT                  = COLUMN

END_OBJECT                    = ACQUISITION_LIST_TABLE

OBJECT                        = FRAME_DATA_HEADER

BYTES                       = 2880 /* RECORD_BYTES x RECORDS */

HEADER_TYPE                 = FITS

INTERCHANGE_FORMAT          = ASCII

RECORDS                     = 1

DESCRIPTION                 = "

This is the FITS header for FITS extension number = 3, FITS

extension name = FRAME_DATA"

END_OBJECT                    = FRAME_DATA_HEADER

OBJECT                        = FRAME_DATA_TABLE

INTERCHANGE_FORMAT          = BINARY

ROWS                        = 38

COLUMNS                     = 2

ROW_BYTES                   = 65544

DESCRIPTION                 = "

All data from the LAMP science data file received from the LRO MOC

except for the file header.  The data from the file header are

copied into the header of this extension.  For the nominal pixel

list and histogram data cases, this extension contains a series of

complete LAMP data frames as specified in the LAMP instrument ICD

and the LAMP Software User's Manual."

OBJECT                      = COLUMN

NAME                      = "GEN_TIME"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 1

BYTES                     = 8

DESCRIPTION               = "

Frame generation time (seconds since 00:00 UTC, 01 Jan 2001)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "FRAME_DATA"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 9

BYTES                     = 65536

ITEMS                     = 32768

ITEM_BYTES                = 2

DESCRIPTION               = "

This column contains the 32768 2-byte words of the raw science

data frame generated by the LAMP instrument.  The correct

interpretation of the data contained in the frame depends on the

instrument mode when the data were taken (PIXELLIST or HISTOGRAM).

Please consult the LAMP instrument ICD and the LAMP Software

User's Manual for details about how to interpret the frame

contents."

END_OBJECT                  = COLUMN

END_OBJECT                    = FRAME_DATA_TABLE

OBJECT                        = CALCULATED_COUNTRATE_HEADER

BYTES                       = 2880 /* RECORD_BYTES x RECORDS */

HEADER_TYPE                 = FITS

INTERCHANGE_FORMAT          = ASCII

RECORDS                     = 1

DESCRIPTION                 = "

This is the FITS header for FITS extension number = 4, FITS

extension name = CALCULATED_COUNTRATE"

END_OBJECT                    = CALCULATED_COUNTRATE_HEADER

OBJECT                        = CALCULATED_COUNTRATE_TABLE

INTERCHANGE_FORMAT          = BINARY

ROWS                        = 12498

COLUMNS                     = 3

ROW_BYTES                   = 16

OBJECT                      = COLUMN

NAME                      = "HACK_TIME"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 1

BYTES                     = 4

DESCRIPTION               = "

Hack time at start of interval (wrap extended)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "SCUT_TIME"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 5

BYTES                     = 8

DESCRIPTION               = "

Hack time converted into spacecraft UTC (seconds since 00:00 UTC,

01 Jan 2001)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "COUNT_RATE"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 13

BYTES                     = 4

DESCRIPTION               = "

Countrate for the interval (Hz)"

END_OBJECT                  = COLUMN

END_OBJECT                    = CALCULATED_COUNTRATE_TABLE

OBJECT                        = LTS_DATA_HEADER

BYTES                       = 2880 /* RECORD_BYTES x RECORDS */

HEADER_TYPE                 = FITS

INTERCHANGE_FORMAT          = ASCII

RECORDS                     = 1

DESCRIPTION                 = "

This is the FITS header for FITS extension number = 5, FITS

extension name = LTS_DATA"

END_OBJECT                    = LTS_DATA_HEADER

OBJECT                        = LTS_DATA_TABLE

INTERCHANGE_FORMAT          = BINARY

ROWS                        = 2700

COLUMNS                     = 4

ROW_BYTES                   = 14

OBJECT                      = COLUMN

NAME                      = "HACK_TIME"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 1

BYTES                     = 4

DESCRIPTION               = "

Hack time at start of interval (wrap extended)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "SCUT_TIME"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 5

BYTES                     = 8

DESCRIPTION               = "

Hack time converted into spacecraft UTC (seconds since 00:00 UTC,

01 Jan 2001)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "LTS_A"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 13

BYTES                     = 1

DESCRIPTION               = "

LTS A high rate scaled value"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "LTS_B"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 14

BYTES                     = 1

DESCRIPTION               = "

LTS B high rate scaled value"

END_OBJECT                  = COLUMN

END_OBJECT                    = LTS_DATA_TABLE

OBJECT                        = HOUSEKEEPING_HEADER

BYTES                       = 11520 /* RECORD_BYTES x RECORDS */

HEADER_TYPE                 = FITS

INTERCHANGE_FORMAT          = ASCII

RECORDS                     = 4

DESCRIPTION                 = "

This is the FITS header for FITS extension number = 6, FITS

extension name = HOUSEKEEPING"

END_OBJECT                    = HOUSEKEEPING_HEADER

OBJECT                        = HOUSEKEEPING_TABLE

INTERCHANGE_FORMAT          = BINARY

ROWS                        = 270

COLUMNS                     = 37

ROW_BYTES                   = 229

OBJECT                      = COLUMN

NAME                      = "SCUT_TIME"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 1

BYTES                     = 8

DESCRIPTION               = "

Spacecraft UTC (seconds since epoch from HK)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "HACK_TIME"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 9

BYTES                     = 4

DESCRIPTION               = "

Extended instrument hack time (since HK on)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "PACK_CNT"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 13

BYTES                     = 2

DESCRIPTION               = "

14-bit packet count (since HK on)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "PACKET_DATA"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 15

BYTES                     = 122

ITEMS                     = 122

ITEM_BYTES                = 1

DESCRIPTION               = "

This column contains the 122 bytes of the raw housekeeping

telemetry packet generated by the LAMP instrument.  Detailed

information needed to decommutate and interpret the packet

contents can be found in the LAMP Software User's Manual."

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "INST_STATE"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 137

BYTES                     = 1

DESCRIPTION               = "

Instrument state (2,6=SAFE, 1,5=CHK, 3=PIX, 7=HIS)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "LAST_SAFETY"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 138

BYTES                     = 1

DESCRIPTION               = "

Last safety (0=none)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "LVPS_STAT"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 139

BYTES                     = 1

DESCRIPTION               = "

Active LVPS (1=A, 2=B, 3=both)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "HVPS_STAT"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 140

BYTES                     = 1

DESCRIPTION               = "

Active HVPS (0=off, 1=A, 2=B, 3=both)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MIRR_TMP_SET"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 141

BYTES                     = 4

DESCRIPTION               = "

Mirror temperature set point (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "GRAT_TMP_SET"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 145

BYTES                     = 4

DESCRIPTION               = "

Grating temperature set point (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MIRR_HTR_STAT"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 149

BYTES                     = 1

DESCRIPTION               = "

Mirror heater status (0=off, 1=A, 2=B, 3=both)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "GRAT_HTR_STAT"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 150

BYTES                     = 1

DESCRIPTION               = "

Grating heater status (0=off, 1=A, 2=B, 3=both)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MIRR_A_TMP"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 151

BYTES                     = 4

DESCRIPTION               = "

Mirror temperature A (primary) (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MIRR_B_TMP"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 155

BYTES                     = 4

DESCRIPTION               = "

Mirror temperature B (redundant) (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "GRAT_A_TMP"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 159

BYTES                     = 4

DESCRIPTION               = "

Grating temperature A (primary) (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "GRAT_B_TMP"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 163

BYTES                     = 4

DESCRIPTION               = "

Grating temperature B (redundant) (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "CDH_ELEC_TMP"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 167

BYTES                     = 4

DESCRIPTION               = "

C&DH electronics temperature (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "DET_HOUS_TMP"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 171

BYTES                     = 4

DESCRIPTION               = "

Detector housing temperature (degrees C)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "APDOOR"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 175

BYTES                     = 1

DESCRIPTION               = "

Aperture door state (1=closed, 2=open, 3=between)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "LTS_DARK"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 176

BYTES                     = 1

DESCRIPTION               = "

LTS dark status (0=light, 1=dark)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "STIM_STAT"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 177

BYTES                     = 1

DESCRIPTION               = "

STIM status (0=off, 1=on)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "HV_SETPNT"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 178

BYTES                     = 4

DESCRIPTION               = "

Detector HVPS setpoint (kVolt)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MCPV1"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 182

BYTES                     = 4

DESCRIPTION               = "

Detector MCP voltage 1 (kVolt)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "ANODEV1"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 186

BYTES                     = 4

DESCRIPTION               = "

Detector anode voltage 1 (kVolt)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "STRIPI1"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 190

BYTES                     = 4

DESCRIPTION               = "

Detector strip current 1 (uA)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MCPV2"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 194

BYTES                     = 4

DESCRIPTION               = "

Detector MCP voltage 2 (kVolt)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "ANODEV2"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 198

BYTES                     = 4

DESCRIPTION               = "

Detector anode voltage 2 (kVolt)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "STRIPI2"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 202

BYTES                     = 4

DESCRIPTION               = "

Detector strip current 2 (uA)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MAX_MCPV"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 206

BYTES                     = 4

DESCRIPTION               = "

Maximum MCP voltage last second (kVolt)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "MAX_STRIPI"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 210

BYTES                     = 4

DESCRIPTION               = "

Maximum summed strip current last second (uA)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "DISCRIM"

DATA_TYPE                 = IEEE_REAL

START_BYTE                = 214

BYTES                     = 4

DESCRIPTION               = "

Detector discriminator voltage (volt)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "COUNT_RATE"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 218

BYTES                     = 4

DESCRIPTION               = "

Analog (raw) countrate (Hz)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "RAW_LTS_A"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 222

BYTES                     = 2

DESCRIPTION               = "

Raw LTS A (14 bits, raw counts)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "RAW_LTS_B"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 224

BYTES                     = 2

DESCRIPTION               = "

Raw LTS B (14 bits, raw counts)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "LTS_CYCLES"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 226

BYTES                     = 1

DESCRIPTION               = "

LTS safing cycles in acquisition"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "SAFETY"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 227

BYTES                     = 1

DESCRIPTION               = "

Current safety status (0=none pending)"

END_OBJECT                  = COLUMN

OBJECT                      = COLUMN

NAME                      = "SAFE_TIMER"

DATA_TYPE                 = MSB_UNSIGNED_INTEGER

START_BYTE                = 228

BYTES                     = 2

DESCRIPTION               = "

Safety timeout timer (seconds remaining)"

END_OBJECT                  = COLUMN

END_OBJECT                    = HOUSEKEEPING_TABLE

END